## Slide 1: Electric Cars
13.12.2011
Elena Zarkh
Jasmin Merzel
Jonathan Ottnad

## Slide 2: Overview
Historical Introduction
Concept of Electric Cars
Batteries, engine and brakes
CO2-savings
Monetary savings
Infrastructure
Future development
Conclusion

## Slide 3: Historical introduction
1672 first automobile (steam engine, Ferdinand Verbiest )
1828 first electric car model, Ányos Jedlik
Between 1832-1838 first electric carriage, R. Anderson
1842 first electric car with a non-rechargeable
electric cell, Thomas Davenport and Robert Anderson
1885 the first car with four-stroke circle gasoline engine, Karl Benz
1891 first electric car that actually worked, A. L. Ryker and W. Morrison
Notes: 1920: electric cars had to competite with petroleum-fueled cars

## Slide 4: Historical introduction
1897 first commercial application
1899 first world speed record of 105 km/h
Camille Jenatzy in his car Jamais Contente,
Top speed of 105.88 km/h on April 29, 1899
www.wikipedia.org
Notes: 1920: electric cars had to competite with petroleum-fueled cars

## Slide 5: Historical introduction
1935 practically disappeared
The energy crisis in the 1970’s and 80’s revivals the interest
In the 90’s high interest for the “emissions free vehicles”:
  New technologies in electric car industry
  The topic of the environment pollution is still relevant

## Slide 6: Historical introduction
Eliica vs. Porsche 911 Turbo:

## Slide 7: Concept of electric cars
http://www.electronica.mkg

## Slide 8: Concept of range extended electric car
www.opel.de
Notes: Rein elektronischer range: 60 km

## Slide 9: Batteries, engine and brakes
Battery types:
 24 kWh Lithium-ion Battery: 190 kg, 8400 €
 | Cost per Wh | Wh / kg | Wh / liter
Lead-acid | 0.13 € | 41 | 100
Nickel-metal | 0.72 € | 95 | 300
Lithium-ion | 0.35 € | 128 | 230

## Slide 10: Batteries, engine and brakes
Engine types:
AC-Induction
DC-Brushes
Both types can be:
Wheel-hub-engine
Direct-drive-engine

## Slide 11: Batteries, engine and brakes
Brakes:
Regenerative brake
Can extend range up to 30%
Useful for stop&go
www.electric-car-abc.com

## Slide 12: CO2-savings
CO2-emission of fossile-energy powered vehicle: about 160 g/km (average mid-class car)
What causes the emission of an electric car?
  The production of energy used to charge the electric car
Where does this energy come from?

## Slide 13: CO2-savings
 563 g/kWh CO2-Emission

## Slide 14: CO2-savings
Nissan Leaf:
range: 175.5 km
engine power: 80 kW
max. speed: 140 km/h
battery capacity: 24 kWh
charging efficiency: 85%
 0.161 kWh/km
 90.58 g/km
http://www.car-addicts.com
How much energy does a electric vehicle need?

## Slide 15: CO2-savings
Comparison to other latest electric vehicles:
 | Ford Focus Electric | Chevrolet Chevy Volt* | Mitsubishi i-MIEV | Smart ED
release date | 2012 | 2011 | 2010 | 2009
engine power | 92 kW | 111 kW | 49 kW | 30 kW
max. speed | 135 km/h | 161 km/h | 130 km/h | 100 km/h
battery capacity | 23 kWh | 16 kWh | 16 kWh | 16.5 kWh
range | 160 km | 80 km | 150 km | 135 km
CO2 / km | 95 g/km | 132 g/km | 71 g/km | 81 g/km
Notes: 92 kW = 125 PS

## Slide 16: Monetary savings
Nissan Leaf vs. Nissan Micra:
Average price of 1 liter fuel: 1.52 €
Average price of 1 kWh: 0.17 €
Batteries need to be exchanged after some time
 | Leaf | Micra
engine power | 80 kW | 72 kW
max. speed | 140 km/h | 180 km/h
consumption | 0.161 kWh/km | 0.05 l/km
costs per 100 km | 2.74 € | 7.60 €
price | 37 000 € | 13 000 €

## Slide 17: Infrastructure
Are there enough charging stations?
Can the existing energy production and energy grid cover the arising demand?
What can one do if running out of energy on a trip?

## Slide 18: Infrastructure
Charging stations:
All vehicles can be charged at home
More than 2200 charging stations all over Germany
www.lemnet.org

## Slide 19: Infrastructure
Let us assume a homogenous density of charging stations
Area of Germany: ~ 360 000 km²
1 charging station / 167 km²
Divide Germany in square areas of 167 km² with a charging station at the center
13 km from charging station to charging station
This result is ok with the range of electric cars!
But there are no more than 6 charging slots per charging station at the moment

## Slide 20: Infrastructure
Is the grid ready for electric cars?
In the smart grid the batteries will play an important role
Today most power plants throttle energy production at night
Renewable energies are not reliable
Breakdown service:
Provided by manufacturer only at the moment
Breakdown service people need special technical education

## Slide 21: Future development
Solar supported vehicles
More efficient engines
Faster charging
Batteries with higher capacity

## Slide 22: Future development
Refillable Batteries:
http://www.greenmotorsblog.de

## Slide 23: Conclusion I
Qualified for the city (short distances)
  Less loud
  Does not have any exhaust gas (it still adds to CO2- emissions to the environment )
Monetary savings
Less emissions

## Slide 24: Conclusion II
Less loud -> it is dangerous for walkers
Only for short distances
Long recharge time
Not enough electricity
Better insulation for the electric car (for outdoor temperature)
High-voltage source
No breakdown-service
Expensive: cars as well as batteries and its service

## Slide 25: Sources
www.autobild.de
http://theinstitute.ieee.org/ieee-roundup/opinions/ieee-roundup/electric-vehicles-possibilities-challenges-and-their-impact
http://www.paulchefurka.ca/Electric%20Cars%20and%20CO2.html
http://www.chevrolet.com/volt-electric-car/
http://www.alle-autos-in.de/
http://www.lemnet.org/
www.umweltbundesamt.de

## Slide 26: Sources
http://en.wikipedia.org/wiki/Electric_car
http://inventors.about.com/od/estartinventions/a/History-Of-Electric-Vehicles.htm
http://www.directoryarc.com/articles/2/1/The-Journey-of-Electric-Vehicles-From-Then-to-Now/Page1.html
http://inventors.about.com/od/estartinventions/a/Electric-Vehicles.htm
http://inventors.about.com/od/cstartinventions/a/History-Of-Electric-Vehicles.htm
http://en.wikipedia.org/
http://electric-car-abc.com

## Slide 27: Sources
http://auto.howstuffworks.com/electric-car3.htm
http://www.howstuffworks.com/hybrid-car.htm
http://www.elektroauto-start.de/wissen/elektro-vs-hybrid
http://www.klima-wandel.com
http://www.eliica.com
http://www.stromvergleich.de/elektroauto
http://www.handelsblatt.com/auto/test-technik/batterie-statt-brennkammer/4179482.html?p4179482=all
http://www.elektroauto-hybridauto.de
http://batteryuniversity.com/learn/article/cost_of_power
http://www.allaboutbatteries.com/Battery-Energy.html

## Slide 28
http://www.treehugger.com
http://www.greenmotorsblog.de/
“Who killed the electric car” – Chris Paine, 2006